## Slide 1: Update of the Deployment of BATS Code
Raymond W. Yeung
Institute of Network Coding
The Chinese University of Hong Kong
n-hop technologies
Hong Kong

## Slide 2: Smart Lamppost Connectivity
Smart lampposts must be connected to the Internet backbone
Possible technologies
  optical fiber
  4G
  BATS

## Slide 3: Optical Fiber
Pros
  very high data rate
  highly reliable
Cons
  high installation cost
  very long setup time
  very disrupting process
  sometimes not possible
Realistically only a small number of lampposts can be connected by optical fiber
The rest still need to be connected to the Internet

## Slide 4: How about 4G?
A 4G card is installed at each lamppost
Pros
  easy to deploy
  relatively inexpensive
Cons
  high recurrent cost
  bandwidth drops drastically during rush hours

## Slide 5
BATS: The Multi-hop Solution
optical
fiber

## Slide 6: Why BATS?
Multi-hop is a longstanding problem in wireless communication
Transmission can sustain no more than a few hops if data packets are treated as commodities
The multi-hop curse
BATS is an advanced network coding technology that can sustain tens or even hundreds of hops, without relying on link-by-link retransmission (very bad for video transmission)
Recoding is employed at the intermediate nodes
With BATS, a very long multi-hop network can be realized

## Slide 8: Performance Comparison
Chart: Number of hops, n
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50
BATS | 0.8 | 0.77387 | 0.76104 | 0.75282 | 0.74684 | 0.74219 | 0.7384 | 0.73527 | 0.73253 | 0.73018 | 0.72809 | 0.72617 | 0.7245 | 0.72297 | 0.72153 | 0.72019 | 0.71898 | 0.71787 | 0.71681 | 0.7158 | 0.71484 | 0.71392 | 0.71308 | 0.71231 | 0.71156 | 0.71083 | 0.71013 | 0.70945 | 0.7088 | 0.70817 | 0.70755 | 0.70699 | 0.70646 | 0.70595 | 0.70545 | 0.70496 | 0.70448 | 0.70401 | 0.70355 | 0.70311 | 0.70267 | 0.70224 | 0.70183 | 0.70142 | 0.70103 | 0.70068 | 0.70033 | 0.69999 | 0.69965 | 0.69932
TCP/IP | 0.8 | 0.64 | 0.512 | 0.4096 | 0.32768 | 0.26214 | 0.20972 | 0.16777 | 0.13422 | 0.10737 | 0.085899 | 0.068719 | 0.054976 | 0.04398 | 0.035184 | 0.028147 | 0.022518 | 0.018014 | 0.014412 | 0.011529 | 0.0092234 | 0.0073787 | 0.005903 | 0.0047224 | 0.0037779 | 0.0030223 | 0.0024179 | 0.0019343 | 0.0015474 | 0.0012379 | 0.00099035 | 0.00079228 | 0.00063383 | 0.00050706 | 0.00040565 | 0.00032452 | 0.00025961 | 0.00020769 | 0.00016615 | 0.00013292 | 0.00010634 | 8.5071e-05 | 6.8056e-05 | 5.4445e-05 | 4.3556e-05 | 3.4845e-05 | 2.7876e-05 | 2.2301e-05 | 1.7841e-05 | 1.4272e-05

## Slide 9: Performance Comparison
Chart: Number of hops, n

## Slide 10: Technical Features
high throughput
low latency
low coding complexity
low storage requirement





## Slide 11: Hong Kong Smart Lamppost Project

## Slide 12: Pilot Project
Installation of 400 smart lampposts starting summer 2019
Followed by several 10,000 lampposts
n-hop has been commissioned to deploy BATS in 36 out of the first 50 smart lampposts

## Slide 14
Participated in the 47th International Exhibition of Inventions of Geneva, 2019:
“Wireless Multi-hop Network for Smart Lampposts”
Awarded a Gold Medal with Congratulations of the Jury

## Slide 15
co-developed with
Photo for reference only

## Slide 16: Current Status
Successfully deployed at two streets
  one street heavily vandalized during a protest on 8/24
Almost done at another street
The general public has concern about the installation of video cameras on the lampposts due to possible infringement of privacy
The Government has formed a special committee to review the smart lampposts applications
One possible recommendation is to replace the cameras by radars or lidars

## Slide 17: BATS + Fog Computing
BATS is inherently a fog computing application because the computation must be done at the edge
Plan to install 20 fog computing based smart lampposts on the CUHK campus, with BATS being provided as a service by the fog node
A prototype for next generation smart lampposts

## Slide 18: Further Opportunities
The HK Government is interested in installing smart lampposts in the country parks (largely not covered by celluar) for providing WiFi services to hikers
Many cities in Southeast Asia are interested in pilot smart lamppost projects

## Slide 19: Internet Draft Submitted
BATS Coding Scheme for Multi-hop Data Transport
draft-yang-nwcrg-bats-00 (Oct 21, 2018)
Prepared by
Shenghao Yang, Xuan Huang
The Chinese University of Hong Kong, Shenzhen
Raymond W. Yeung
The Chinese University of Hong Kong
John K. Zao
National Chiao Tung University

## Slide 20: BATS IPs
3 US patents
  US Patent No. 8,693,501
  US Patent Application No. 14/871,257
  US Patent No. 10,237,782
6 EU patents
  DE validation of EP Patent No. 2644004
  FI validation of EP Patent No. 2644004
  FR validation of EP Patent No. 2644004
  GB validation of EP Patent No. 2644004
  SE validation of EP Patent No. 2644004
2 China patents
  CN Patent No. ZL 201180055775.3
  CN Patent Application no. 201610857698.8

## Slide 21: The BATS solution
optical
fiber